PCB111000_V1/2 test results

Preliminary tests
4 V1 and 4 V2 pcbs set up using
8_UNO_AVR_Programmer_V3 and 5_Project_pcb_168_V2.30_Arduino_V2.

New System tests

Carried out on all 4 V1 and 4 V2 pcbs

Use 5_Project_pcb_168_V2.30_Arduino_V2 to reload the mini-OS

Step 1	Load 5_Project_pcb_168_V2.30_Arduino_V2 onto the Atmega 168
Step 2	Reload the on-chip strings
Step 3 Reload the Hello world strings
Step 4	Reload the mini-OS and bootloader
Step 5 Recalibrate the Atmega328
Step 6 Run the bootloader and load 3_Division_subroutine check all display segments
Step 7 Load Example 9E
Check Version data
SW information
Hello world read out
Default program
9E program

Display brightness control tested:	Control is week!

Project tests

Recompile all the following examples:
1_first_project and 2_Receiver_Transmitter_Basic examples
2_Receiver_Transmitter_Basic
3_Interrupts_and_switches examples
4_binary_and_bit_operations

1_first_project examples	tested on PCB111000_V2:1 (CA)
2_Receiver_Transmitter_Basic	tested on PCB111000_V2:1 (CA)
3_Interrupts_and_switches	All tested on PCB111000_V2:1 (CA)

4_binary_and_bit_operations