PCB_111000_V2

Introduction

PCB_111000_V2 is a development of PCB_111000.
Both pcbs are loaded with
An Atmega 168 which hosts user projects

An Atmega 328. This hosts a mini-OS which:
Drives an 8 digit display
Hosts a pcb bootloader that programs the Atmega 168
Provides a variety of services for use by user projects

Differences are:
For the HW
The FETS used to drive the display are no longer fitted
For the SW
User projects are now compiled using Arduino
System programs are compiled using Studio 7
PCB initialisation is carried out using two Arduino sketches rather than bespoke HW
Note
The winAVR compiler which was originally used is no longer supported.

Setting up PCB-111000_V2

The two Arduino sketches used to setup PCB-111000_V2 are

8_UNO_AVR_programmer_V3
5_Project_pcb_168_V2.30_Arduino_V2

Step 1	The PCB is loaded with all components except the displays and the Atmega devices

Step 2
Upload 8_UNO_AVR_programmer_V3 to a UNO.

Step 3
With the aid of the Br@y++ terminal emulator use the UNO to:
Upload “5_Project_pcb_168_V2.30_Arduino_V2” to the Atmega 168
Calibrate is internal RC oscillator
Allow the Atmega 168 to run so that it can upload string data to its EEPROM.
Note:
Terminal emulator runs at 38.4KB and uses default settings.

Step 4
Load the Atmega devices onto the PCB11100

Step 5
“5_Project_pcb_168_V2.30_Arduino_V2” under the control of Br@y++ is used to setup the Atmega 328 by:
Uploading the mini-OS to its flash
Uploading the “Hello world” strings to its EEPROM
Checking the calibration of its internal RC oscillator.