1.	Add	#define T0_delay_125us 3,240	to I2C_V25_0_CA_header file.h

2. In file Mini-OS_V25_CA.c
Change line
else {timer_T0_sub_with_interrupt(T0_delay_500us);
to	else {timer_T0_sub_with_interrupt(T0_delay_125us);

In file I2C_V22_0_ISR_subroutines.c
Change
if(eeprom_read_byte((uint8_t*)0x3FB) == 0x01){	//Low level brightness
if(!(T0_interupt_cnt)){
if(mode == 'F') {
TIMSK2 &= (!((1 << OCIE2A) | (1 << TOV2)));
sei();
Display_driver();
TIMSK2 |= ((1 << OCIE2A) | (1 << TOV2));}
else {Display_driver(); }}

switch (MUX_cntl){
case 0: TCNT0 = 194; break;	//500uS period
case 1:	TCNT0 = 128; break;	//1mS period CHECK
case 2: TCNT0 = 69; break;	//1500uS period CHECK
case 3: TCNT0 = 0; break;	//2mS period
case 4: TCNT0 = 178; break;	//2500uS period
case 5: TCNT0 = 162; break;	//3mS period
case 6: TCNT0 = 100;break;	//5ms period
case 7: TCNT0 = 194;break;	//8ms period
default: TCNT0 = 194; break;}	//500uSS period

switch(T0_interupt_cnt){
case 0: T0_interupt_cnt = 1;break;
case 1: {clear_display;} T0_interupt_cnt = 2; break;
case 2: T0_interupt_cnt = 3; break;
case 3: T0_interupt_cnt = 0; break;}
}}

To
if(eeprom_read_byte((uint8_t*)0x3FB) == 0x01){	//Low level brightness
if(!(T0_interupt_cnt)){
if(mode == 'F'){
TIMSK2 &= (!((1 << OCIE2A) | (1 << TOV2)));
sei();
Display_driver();
TIMSK2 |= ((1 << OCIE2A) | (1 << TOV2));}
else {Display_driver(); }}
TCNT0 = 240;

switch(T0_interupt_cnt){
case 0: T0_interupt_cnt = 1;break;
case 1: {clear_display;} T0_interupt_cnt = 2; break;
case 2: T0_interupt_cnt = 3; break;
case 3:
case 4:
case 5:
case 6:
case 7:
case 8:
case 9:
case 10:
case 11:
case 12:
case 13:
case 14: T0_interupt_cnt++; break;
case 15: T0_interupt_cnt = 0; break;}}

Notice that T0_interupt_cnt does not appear to be properly initialised
Add the line T0_interupt_cnt = 0; to #define I2C_Tx_LED_dimmer

Note: Multiplexer demo will not function

Crystal accuracy

30 seconds in 18 hours
i.e. 40 seconds in 24 hours
accuracy is 0.0465

crystal timer counts to 4096 in 1 sec
count to 4095 gives 0.024% increase in speed

Mux modes
Normal
2 cycle time	16	x1	125u +1875	2	16
4	32	x2	250u +3750	4	32
6	48	x3	375u + 5625	6	48
8	64	x4	500 + 7500	8	64
10	80	x5	625 + 9375	10	80
12	96	x6	750 + 11250	12	96
20	160	x10	1250 + 18750	20	160
33	264	x16.5	2000 + 30000	32	264

T0:
Drive at	8000KHz
Use	1024 prescaler
Gives a clock of	7.8125KHz
count = Clock x Time
Count to 255 in	32.64mS

count = Clock x Time

250uS delay = 0.125ms
Prescaler = 4 gives /256
clock = 31.25KHz
count = 7.8125 i.e. 8 gives delay of 256us
Set TCNT0 to 256 – 8 = 248

1.750ms
Count of 8 * 7 = 56
Set TCNT0 to 256-56 = 200
Delay is 1.92ms

125uS delay = 0.125ms
Prescaler = 3 gives /64
clock = 125KHz
count = 15.625 i.e. 16 gives delay of 128us
Set TCNT0 to 256 – 16 = 240

1.875ms
Count of 16 * 15 = 240
Set TCNT0 to 256-240 = 16
Delay is 1.92ms

/******************************/

250us
Prescaler = 4 gives /256
clock = 31.25KHz
in 250us counts to 7.8125 i.e. 8
Set TCNT0 to 248	Delay is 256us

3750us
count to 120
Set TCNT0 to 136	Delay is 3.84ms

/******************************/
375us
Prescaler = 4 gives /256
clock = 31.25KHz
in 375us counts to 11.7 i.e. 12
Set TCNT0 to 244	Delay is 384us

5625us
Set TCNT0 to 76	Delay is 5.76ms

/******************************/

500uS
Prescaler = 4 gives /256
clock = 31.25KHz
in 500us counts to 15.6 i.e.16 Delay is 512us
Set TCNT0 to 240

7500us
Set TCNT0 to 16	Gives delay of 7.68m

/******************************/

625us
Prescaler = 5 gives /1024
clock = 7.8125KHz
In 625us counts to 4.88 i.e. 5
Set TCNT0 to 251 Delay is 640us

9375us
Set TCNT0 to 181	Delay is 9.6ms

/******************************/

750us
Prescaler = 5 gives /1024
clock = 7.8125KHz
in 750us counts to 5.859 i.e. 6
Set TCNT0 to 250	Delay is 768us

11250us
Set TCNT0 to 166	Delay is 11.52ms

/******************************/

1250us
Prescaler = 5 gives /1024
clock = 7.8125KHz
In 1250us counts to 9.76 i.e.10
Set TCNT0 to 246	Delay is 1280us

18.75ms
Set TCNT0 to 106	Delay is 19.2ms

/******************************/
2ms
Counts to15.625 i.e. 16
Set TCNT0 to 240	Delay is 2.048ms
30ms
Count to 240
Set TCNT0 to 16	Delay is 30.72ms

SET bootloader to erase after detecting the “:” at the start of the first line

Update Version info

New file names

Original file names
saves under Github\PCB-111000_V2
Mini-OS_V1\Mini-OS_V23_CA\ OK
Mini-OS_V1\Mini-OS_V24_CC\ OK
Mini-OS_V2\Mini-OS_V25_CA\ OK
Mini-OS_V2\Mini-OS_V26_CC\ OK	Note: all use the same Resources file

Mini-OS_V1_IC\Mini-OS_V27_CA\ OK
Mini-OS_V1_IC\Mini-OS_V28_CC\ OK
Mini-OS_V2_IC\Mini-OS_V29_CA\ OK
Mini-OS_V2_IC\Mini-OS_V30_CC\ OK	Projects all built and copied from V23 to V26

Replace individual resources folder with a shared Mini-OS_Resources folder
Mini-OS_V1 and V2 updated OK.

Note Optimise on level -01

Changes effect	ISR_subroutines.c
and	mode_definitions.h	Common to all versions
Add to Mini-OS_resources and version 2 files

Note line T0_interupt_cnt = 0; added to macro #define I2C_Tx_LED_dimmer \

Add Timer definitions to the Mini-OS project header files

Changes to bootloaders
Erase flash after sending new hex file, not after keypress p at p/r prompt

Mini-OS_V1_bootloaders
2_pcb_Bootloader_V4_25_CA
2_pcb_Bootloader_V4_26_CC

Mini-OS_V2_bootloaders
2_pcb_Bootloader_V4_27_CA
2_pcb_Bootloader_V4_28_CC

USE Optimize for size (-Os)
AND
Memory settings text = 0x3800
BECOME
Mini-OS_V1_with_IC_bootloaders
2_pcb_Bootloader_V4_29_CA
2_pcb_Bootloader_V4_30_CC

Mini-OS_V2_with_IC_bootloaders
2_pcb_Bootloader_V4_31_CA
2_pcb_Bootloader_V4_32_CC

Combine
Mini-OS_V27_CA	with	2_pcb_Bootloader_V4_29_CA
Mini-OS_V28_CC	with	2_pcb_Bootloader_V4_30_CC
Mini-OS_V29_CA	with	2_pcb_Bootloader_V4_31_CA
Mini-OS_V30_CC	with	2_pcb_Bootloader_V4_32_CC

All bootloaders successfully copied to new versions ready to be modified

Three level brightness control

Eeprom 0x3FF equal
01	High level brightness 2mS on all the time
02	Medium brightness: On for 250uS off for 1750us
03	Low level brightness:	Onn for 125uS off for 1875uS

Mini-OS/bootloader changes completed

Generate Bootloader_resources directory and copy in
HW, SW resources and header file.

Only differences effect LED_ON/OFF macros

Changed Bootloader resources:
2_pcb_Bootloader_V4_29_CA

Recompile and check for no changes

Version 2
Mini-OS_V29_CA	OK
2_pcb_Bootloader_V4_31_CA	OK

Mini-OS_V30_CC	OK
2_pcb_Bootloader_V4_32_CC	OK

Update and test version 1

Mini-OS_V27_CA	OK
2_pcb_Bootloader_V4_29_CA	Updated and recompiled OK .Tested OK

Mini-OS_V28_CC	OK
2_pcb_Bootloader_V4_30_CC	OK

Split mini-OS_header files into general and specific files and update medium intensity setting (Use 350uS in place of 250uS).

Mini-OS_V29_CA	OK
Mini-OS_V30_CC	OK

Mini-OS_V28_CC	OK
Mini-OS_V27_CA	OK
MINI-OS purging of obsolete code

Modes in user projects

I2C_Tx_LED_dimmer();	Mode Q
I2C_TX_328_check();	V
I2C_Rx_get_version_A('0');	P
Read_Hello_world_string_A();	H

I2C_Tx_2_integers	1
I2C_Tx_any_segment_clear_alI	2
I2C_Tx_any_segment	3
I2C_Tx_long	6

I2C_Tx_Bwops	G
I2C_Tx_8_byte_array	4
I2C_Tx_display_char	5

I2C_Tx_OS_timer	CDEF
I2C_Tx_Clock_command	CDEF
I2C_initiate_10mS_ref()	CDEF

I2C_Tx_float_num	K
I2C_displayToNum	I

I2C_initiate_7_8125mS_ref	(Cals 168)	U
manual_cal_PCB_A_device();	(328)	N
scan_328_cal_factors	M

PCB_test	O
Multiplexer_demo;	L

I2C_Tx_display():	Uses I2C_Tx_2_integers
display_8_digit_num_string()	Uses I2C_Tx_8_byte_array
display_FPN_short()	Uses I2C_Tx_8_byte_array()
I2C_FPN_to_display	Uses I2C_Tx_float_num

Modes in mini-OS
1	I2C_Tx_2_integers;
2	I2C_Tx_any_segment;
3	I2C_Tx_any_segment;
4	I2C_Tx_8_byte_array
5	I2C_Tx_display_char;
6	I2C_Tx_long;
7	I2C_Tx_Compile_tables();	obsolete
8	I2C_Tx_2URNs_from_IO ();	Obsolete
9	I2C_Tx_Uarithmetic_OP ();	Obsolete
A	I2C_Tx_accumulator_1()	Obsolete
B	I2C_Tx_accumulator_2()	Obsolete
C	Clock
D	Clock
E	Clock
F	Clock
G	I2C_Tx_BWops;
H	Message_from_the_OS();
I	I2C_displayToLong;
J	I2C_Tx_real_num;
K	I2C_Tx_float_num;
L	Multiplexer_demo;
M	cal_plot_328();
N	manual_cal_PCB_A_device();
O	PCB_test
P	I2C_Rx_get_version;
Q	I2C_Tx_LED_dimmer;
U	start_T2_for_ATMEGA_168_cal(1)
V	set_diagnostic_mode;

W	restore_168_EEPROM_strings; OBSOLETE
X	cal_spot_check();
Y	Trash cal bytes	OBSOLETE
Z	Transmit OSCCAL