Development of Github_PCB-111000

Create new folders	9_Nano_Projects
and	Resources_nano_projects

Go to	ATMEGA_project_work_BKP_30_Sept_2022\I2C_apps_project_V10	and
Copy the files in	2_User_projects_V1_9\Resources_V12 to Resources_nano_projects

Create a new Arduino project	1_first_project
and save it under	9_Nano_Projects
Note that folder	1_first_project	is created for the project

Open	2_User_projects_V1_9\….\….\Open Proj_1A1
Copy its contents into the Arduino project

Copy	Proj_1A1 hex file and
Proj_1A1_header_file
into the	1_first_project folder along side the 1_first_project project
Rename the header file	First_project_header

Initial tests

Upload the hex file to a PCB111000
Check it runs immediately following an -r- keypress
Gives Version data following an -x- keypress

Close and reopen the Arduino Project so that it includes the header file
Edit the #include statement to read	#include "First_project_header.h"

Compile the project using Nano board Atmega 168 processor
Using	setup_HW_basic;
and	setup_HW

Check the following text is printed out OK
1 for OS version
2 for system data
3 Message from the OS (x to escape)
The Default project runs correctly

OS version
OS: I2C_V20_0_CA

System data:
SW information: Operating system I2C_V20_0_CA Projects V1_9 and Bootloader V4_21_CA. External programmer V2_30B
Actual operating system is Github_PCB-111000_V2\Mini-OS_V22

Update mini-OS

Github_PCB-111000 contains mini-OS version12 and 13.
Replace this OS with mini-OS_Version 20 copied from
ATMEGA_project_work_BKP_30_Sept_2022\I2C_apps_project_V10
Rebuilding mini-OS_V20 will require use of Atmel Studio 7.
Reprogramming the Atmega 328 with require the programs saved under
ATMEGA_project_work_BKP_30_Sept_2022\I2C_apps_project_V10

To update the mini-OS	DO NOT EXPECT TO NEED TO DO THIS
At the p/r prompt put “4_Project_pcb_168_V2.30B” on the Atmega 168
At the ‘P’ prompt press
‘P’ to reprogram the mini-OS
‘E’ to update the “Hello world” file.

Note: Other programmers that should no longer be needed.
Version A: Same as Version B but B has one extra line to trigger auto cal of the 328.
4a_Project_pcb_328_V2.31A runs on an Atmega328
Programmer_pcb_328_V1.10 runs on a 328 and is used to put V2.30B on a 168 or replicate	itself on another 328
6_BL_programmer_V1_5 was a development tool and is no longer required

If more boards are to be built a UNO will be used to put V2.30B onto an Atmega 168 and also calibrate it.

The Atmega 328 programmer applies the following config bytes to the 168

FF	D5	C2	EB
V1.10 applies	FF	D7	E2	EB

Differences effect the brown out level and start up time.

New locations for user cal bytes	Check carefully that these are always used

0x1FF	User calibration byte
0x1FE	User calibration byte
0x1FD	Default calibration byte

0x1FC PRN generator random number HB
0x1FB PRN generator random number LB
Note: Only two locations are used here but write to EEPROM every 45 secs

2_User_projects_V1_9\Proj_9_System_projects\Proj_9A_168_manual_cal()
writes EEPROM location 0x1FA to zero.
No reason for this has been found and the line should be commented out

Problems
1	Note old problem with redefinition of
volatile char PCMSK0_mem, PCMSK2_mem;
in File I2C_subroutines_2
void I2C_Tx_float_display_control(void)
and #include "../Header_files/I_O_from switches.h"
Solution copied from PCB111000_UNO Compiles OK but not fully tested.
2	I2C_subroutines_2 line 121	SOLVED
Commented out for time being.
Calibration programs	All OK
Copy the following two calibration routines to
9_Nano_Projects\System_programs
2_User_projects_V1_9\Proj_9A_168_manual_cal
and \Proj_9B_168_auto_cal

Compile with Arduino_nano_168 and calibrate two pcbs successfully.
Note Problem 2 above

Note: The Atmega 328 (mini-OS device calibrates itself automatically at every POR)
provided the DPDT is switched to the right.

1_first_project	12 examples

Example 1	Ramp with SW reset	Tested OK
Example 1A	Ramp with WDT generated reset	Tested OK
Example 2	Back and forth with WDT	Tested OK
Example 3	Chase	(spurious wdr(); removed)	Tested OK
Example 4	Single ellipse	(spurious wdr(); removed)	Tested OK
Example 5	Double ellipse	(spurious wdr(); removed)	Tested OK
Example 6	Upper/lower see saws	Tested OK
Example 7	Moving top	Tested OK
Example 7A	Moving top (with reset on sw3)	Tested OK
Example 8	Leds leapfrog	WDT added	Tested OK
Example 9	LEDS light up in random order (with reset)	Tested OK
Example 10	Default program with WDT	Tested OK

Tested with setup_HW_extra
Example_1	Modes 0 – 4 tested OK	Saved as Example_1E
Example_4	Modes 0 – 4 tested OK	Saved as Example_4E
Example_7	Modes 0 – 4 tested OK	Saved as Example_7E
Example_9	Modes 0 – 4 tested OK	Saved as Example_9E

2_Receiver_Transmitter_Basic

Example_1	Tested OK
Example_2	Tested OK
Example_3	Tested OK
Example_4	Reset implemented	Tested OK
Example_5	Reset implemented	Tested OK
Example_6	Reset implemented	Tested OK
Example_7	Tested OK
Example_8	Tested OK
Example_9	Tested OK

Tested with setup_HW_extra
Example_1
Example_3
Example_5
Example_7

3_Interrupts_and_switches
Basic HW	HW_Extra
3A_UART_timer_interrupts	OK	OK
3B_Pin_Change_Interrupt	OK	OK
3C_reaction_time_tester	OK	OK
3D_timer_PCI_interrupts	OK	OK
3E_Keypress_logger	OK	OK
3F_Prime_numbers	OK	OK
3G_Prime_numbers_plus	OK	OK

4_binary_and_bit_operations

1_Bit_ops_1	OK	OK
2_Bit_ops_2	OK	OK
3_Division_subroutine	OK	OK
4_Char_to_binary	OK	OK

5_Timers	Performance degraded by tendency of I2C bus to crash.
Resolved using watch dog with interrupt