1.	Add	#define T0_delay_125us 3,240	to I2C_V25_0_CA_header file.h

2. In file Mini-OS_V25_CA.c
Change line
else {timer_T0_sub_with_interrupt(T0_delay_500us);
to	else {timer_T0_sub_with_interrupt(T0_delay_125us);

In file I2C_V22_0_ISR_subroutines.c
Change
if(eeprom_read_byte((uint8_t*)0x3FB) == 0x01){	//Low level brightness
if(!(T0_interupt_cnt)){
if(mode == 'F') {
TIMSK2 &= (!((1 << OCIE2A) | (1 << TOV2)));
sei();
Display_driver();
TIMSK2 |= ((1 << OCIE2A) | (1 << TOV2));}
else {Display_driver(); }}

switch (MUX_cntl){
case 0: TCNT0 = 194; break;	//500uS period
case 1:	TCNT0 = 128; break;	//1mS period CHECK
case 2: TCNT0 = 69; break;	//1500uS period CHECK
case 3: TCNT0 = 0; break;	//2mS period
case 4: TCNT0 = 178; break;	//2500uS period
case 5: TCNT0 = 162; break;	//3mS period
case 6: TCNT0 = 100;break;	//5ms period
case 7: TCNT0 = 194;break;	//8ms period
default: TCNT0 = 194; break;}	//500uSS period

switch(T0_interupt_cnt){
case 0: T0_interupt_cnt = 1;break;
case 1: {clear_display;} T0_interupt_cnt = 2; break;
case 2: T0_interupt_cnt = 3; break;
case 3: T0_interupt_cnt = 0; break;}
}}

To
if(eeprom_read_byte((uint8_t*)0x3FB) == 0x01){	//Low level brightness
if(!(T0_interupt_cnt)){
if(mode == 'F'){
TIMSK2 &= (!((1 << OCIE2A) | (1 << TOV2)));
sei();
Display_driver();
TIMSK2 |= ((1 << OCIE2A) | (1 << TOV2));}
else {Display_driver(); }}
TCNT0 = 240;

switch(T0_interupt_cnt){
case 0: T0_interupt_cnt = 1;break;
case 1: {clear_display;} T0_interupt_cnt = 2; break;
case 2: T0_interupt_cnt = 3; break;
case 3:
case 4:
case 5:
case 6:
case 7:
case 8:
case 9:
case 10:
case 11:
case 12:
case 13:
case 14: T0_interupt_cnt++; break;
case 15: T0_interupt_cnt = 0; break;}}

Notice that T0_interupt_cnt does not appear to be properly initialised
Add the line T0_interupt_cnt = 0; to #define I2C_Tx_LED_dimmer

Note: Multiplexer demo will not function

Crystal accuracy

30 seconds in 18 hours
i.e. 40 seconds in 24 hours
accuracy is 0.0465

crystal timer counts to 4096 in 1 sec
count to 4095 gives 0.024% increase in speed

Mux modes
Normal
2 cycle time	16	x1	125u +1875	2	16
4	32	x2	250u +3750	4	32
6	48	x3	375u + 5625	6	48
8	64	x4	500 + 7500	8	64
10	80	x5	625 + 9375	10	80
12	96	x6	750 + 11250	12	96
20	160	x10	1250 + 18750	20	160
33	264	x16.5	2000 + 30000	32	264

T0:
Drive at	8000KHz
Use	1024 prescaler
Gives a clock of	7.8125KHz
count = Clock x Time
Count to 255 in	32.64mS

count = Clock x Time

125uS delay = 0.125ms
Prescaler = 3 gives /64
clock = 125KHz
count = 15.625 i.e. 16 gives delay of 128us
Set TCNT0 to 256 – 16 = 240

1.875ms
Count of 16 * 15 = 240
Set TCNT0 to 256-240 = 16
Delay is 1.92ms

/******************************/

250us
Prescaler = 4 gives /256
clock = 31.25KHz
in 250us counts to 7.8125 i.e. 8
Set TCNT0 to 248	Delay is 256us

3750us
count to 120
Set TCNT0 to 136	Delay is 3.84ms

/******************************/
375us
Prescaler = 4 gives /256
clock = 31.25KHz
in 375us counts to 11.7 i.e. 12
Set TCNT0 to 244	Delay is 384us

5625us
Set TCNT0 to 76	Delay is 5.76ms

/******************************/

500uS
Prescaler = 4 gives /256
clock = 31.25KHz
in 500us counts to 15.6 i.e.16 Delay is 512us
Set TCNT0 to 240

7500us
Set TCNT0 to 16	Gives delay of 7.68m

/******************************/

625us
Prescaler = 5 gives /1024
clock = 7.8125KHz
In 625us counts to 4.88 i.e. 5
Set TCNT0 to 251 Delay is 640us

9375us
Set TCNT0 to 181	Delay is 9.6ms

/******************************/

750us
Prescaler = 5 gives /1024
clock = 7.8125KHz
in 750us counts to 5.859 i.e. 6
Set TCNT0 to 250	Delay is 768us

11250us
Set TCNT0 to 166	Delay is 11.52ms

/******************************/

1250us
Prescaler = 5 gives /1024
clock = 7.8125KHz
In 1250us counts to 9.76 i.e.10
Set TCNT0 to 246	Delay is 1280us

18.75ms
Set TCNT0 to 106	Delay is 19.2ms

/******************************/
2ms
Counts to15.625 i.e. 16
Set TCNT0 to 240	Delay is 2.048ms
30ms
Count to 240
Set TCNT0 to 16	Delay is 30.72ms

SET bootloader to erase after detecting the “:” at the start of the first line

Update Version info

New file names

Original file names
saves under Github\PCB-111000_V2
Mini-OS_V1\Mini-OS_V23_CA\
Mini-OS_V1\Mini-OS_V24_CC\
Mini-OS_V2\Mini-OS_V25_CA\
Mini-OS_V2\Mini-OS_V26_CC\	Note: all use the same Resources file

Mini-OS_V1_IC\Mini-OS_V27_CA\
Mini-OS_V1_IC\Mini-OS_V28_CC\
Mini-OS_V2_IC\Mini-OS_V25_CA\
Mini-OS_V2_IC\Mini-OS_V26_CC