PCB_111000_V2

Introduction

PCB_111000_V2 is a development of PCB_111000.
Both pcbs are loaded with
An Atmega 168 which hosts user projects

An Atmega 328. This hosts a mini-OS which:
Drives an 8 digit display
Hosts a pcb bootloader that programs the Atmega 168
Provides a variety of services for use by user projects

Differences are:
For the HW
The FETS used to drive the display are no longer fitted
For the SW
User projects have been revised and are now compiled using Arduino
System programs are compiled using Studio 7
PCB initialisation is carried out using the following Arduino sketches rather than	bespoke HW
8_UNO_AVR_programmer_V3
5_Project_pcb_168_V2.30_Arduino_V2

Setting up PCB-111000_V2

Step 1	The PCB is loaded with all components except the displays and the Atmega devices

Step 2
Open the sketch “8_UNO_AVR_programmer_V3”. Under Tool/Board select Arduino UNO. Connect the UNO to the PC check the port number and upload the sketch.

Step 3
Close the sketch assemble the HW (see next section) and with the aid of the Br@y++ terminal emulator use the UNO to:
Upload “5_Project_pcb_168_V2.30_Arduino_V2” to the Atmega 168
Calibrate is internal RC oscillator
Allow the Atmega 168 to run so that it can upload string data to its EEPROM.
Note:
Terminal emulator runs at 38.4KB and uses default settings.

Step 4
Load the Atmega devices onto the PCB11100

Step 5
Run “5_Project_pcb_168_V2.30_Arduino_V2” under the control of Br@y++ to setup the Atmega 328 by:
Uploading the mini-OS to its flash
Uploading the “Hello world” strings to its EEPROM
Checking the calibration of its internal RC oscillator.

Step 6	Overwrite “5_Project_pcb_168_V2.30_Arduino_V2” with user projects.
Hardware (HW) details

UNO used to program the Atmega168 before it is soldered onto the PCB111000_V2 / Note: Atmega328 pin numbers given for a DIP28 device / Remove Atmega168 before uploading “8_UNO_AVR_programmer_V3” sketch	UNO			Plug-in pcb
	UNO Pin	Atmega 328		Atmega168
		Pin	Function	Pin
	0 (Rx)	2	RXD	2
	1 (Tx)	3	TXD	3

	11	17	MOSI	17
	12	18	MISO	18
	13	19	SCK	19
	A3	26	PC3	1 (Reset)
	GND			8, 22
	5V			7,20
	8	14	PB0	LED driver

Driving “8_UNO_AVR_programmer_V3”

Having uploaded the sketch to a UNO open Br@y++ and set it up as follows:
8 data bits, 1 stop bit, no parity or handshaking and a baud rate of 38.4KB

Click on “scan” to identify the comm port and then click on connect:

The following user prompt should be generated:
“s s s s s s s…………….”

Step 1	Click mouse pointer in the text box (at the bottom of the Br@y++ window) and
press -s- to get
“Atmega 168 detected.
Press -p- to program flash, -r- to run target, -d- to clear the target EEPROM or -x- to	escape.”

Step 2	Press -p- and send “5_Project_pcb_168_V2.30_Arduino_V2.ino.eightanaloginputs”

Step 3	Follow instructions to Cal device the get user prompt “P/S P/S P/S………….”

Step 4	Press -s-, change bit rate when asked and send on-chip_strings

Optional steps
At P/S prompt press -v- to get program name plus version	“Project_pcb_168_V2.30_Arduino”

Reset UNO and change the BR to 38.4kB to restore user prompt	“s s s s s s s…………….”
Press -s- then -d- to clear “on-chip_strings” and cal bytes from Atmega168 EEPROM

Reset UNO to restore user prompt	“s s s s s s s…………….”
Press -s- then -t- to recalibrate the Atmega 328 and restore user prompt “P/S P/S…...…”

Reset UNO to restore user prompt	“s s s s s s s…………….”
Press -s- then -r- to restore user prompt “P/S P/S P/S………….”

Press -s- and reprogram the on-chip strings

Reset UNO to restore user prompt	“s s s s s s s…………….”
Press -s- then -x- to escape

Reprogram the Atmega168 and note that it now offers a recalibration

Driving “5_Project_pcb_168_V2.30_Arduino_V2”

Solder the Atmega 168 to the PCB-111000_V2.
Reconnect the pcb to a PC running Br@y++.
The user prompt “P/S P/S P/S…………..”
Press -p- and the response TTND (Target not detected) will be generated.

To upgrade the mini_OS

Push the DPDT switch right and press the reset switch.
Press -p- at the “p/r p/r p/r p/r p/r….” user prompt
and send 5_Project_pcb_168_V2.30_Arduino_V2.ino.eightanaloginputs
Run the project to get the “P/S P/S P/S………….” prompt
Press -s- to restore the strings
Press -p- twice to send the new mini-OS.