PCB_111000_V2

Introduction

PCB_111000_V2 is a development of PCB_111000.
Both pcbs are loaded with
An Atmega 168 which hosts user projects

An Atmega 328. This hosts a mini-OS which:
Drives an 8 digit display
Hosts a pcb bootloader that programs the Atmega 168
Provides a variety of services for use by user projects

Differences are:
For the HW
The FETS used to drive the display are no longer fitted
For the SW
User projects are now compiled using Arduino
System programs are compiled using Studio 7
PCB initialisation is carried out using the following Arduino sketches rather than	bespoke HW
8_UNO_AVR_programmer_V3
5_Project_pcb_168_V2.30_Arduino_V2
Note
The winAVR compiler which was originally used is no longer supported.

Setting up PCB-111000_V2

Step 1	The PCB is loaded with all components except the displays and the Atmega devices

Step 2
Upload 8_UNO_AVR_programmer_V3 to a UNO.

Step 3
With the aid of the Br@y++ terminal emulator use the UNO to:
Upload “5_Project_pcb_168_V2.30_Arduino_V2” to the Atmega 168
Calibrate is internal RC oscillator
Allow the Atmega 168 to run so that it can upload string data to its EEPROM.
Note:
Terminal emulator runs at 38.4KB and uses default settings.

Step 4
Load the Atmega devices onto the PCB11100

Step 5
Run “5_Project_pcb_168_V2.30_Arduino_V2” under the control of Br@y++ to setup the Atmega 328 by:
Uploading the mini-OS to its flash
Uploading the “Hello world” strings to its EEPROM
Checking the calibration of its internal RC oscillator.

Hardware (HW) details

Driving “8_UNO_AVR_programmer_V3”

Having uploaded the sketch to a UNO open Br@y++ and set it up as follows:
8 data bits, 1 stop bit, no parity or handshaking and a baud rate of 38.4KB

Click on “scan” to identify the comm port and then click on connect:

The following user prompt should be generated:
“s s s s s s s…………….”

Step 1	Click mouse pointer in the text box (at the bottom of the Br@y++ window) and
press -s- to get
Atmega 168 detected.
“Press -p- to program flash, -r- to run target, -d- to clear the target EEPROM or -x- to	escape.”
Step 2	Press -p-
Send	“5_Project_pcb_168_V2.30_Arduino_V2.ino.eightanaloginputs”
Step 3	Follow instructions to Cal device
Get user prompt “P/S P/S P/S………….”
Step 4	press -s- and change BR and send on-chip_strings

Optional steps
At P/S prompt press -v- to get program name plus version	“Project_pcb_168_V2.30_Arduino”

Reset UNO to restore user prompt	“s s s s s s s…………….”
Press -s- then -d- to clear “on-chip_strings” and cal bytes from Atmega168 EEPROM

Reset UNO to restore user prompt	“s s s s s s s…………….”
Press -s- then -t- to recalibrate the Atmega 328 and restore user prompt “P/S P/S…...…”

Reset UNO to restore user prompt	“s s s s s s s…………….”
Press -s- then -r- to restore user prompt “P/S P/S P/S………….”

Press -s- and reprogram the on-chip strings

Reset UNO to restore user prompt	“s s s s s s s…………….”
Press -s- then -x- to escape

Reprogram the Atmega168 and note that it now offers a recalibration

Driving “5_Project_pcb_168_V2.30_Arduino_V2”

,.,