PCB_111000_1 Set Up

The PCB_111000_1 project hard ware consists of two programming pcbs and the PCB11100_1 project pcb.

The Programming PCB’s

PCB-1: The USBasp programming pcb which consists of
Plug-in solderless breadboard	USBasp programmer
CP2102 micro USB bridge	A watch crystal

The CP2102 micro USB bridge and USB programmer were purchased from E-bay. To identify them search in Ebay under
6 Pin CP2102 Micro USB To UART TTL Module Serial Converter STC For Arduino and
USBASP USB ISP Programmer AVR ATMEL ATMega8 Download Pin IDC Cable 3.3V 5V UK

PCB-2: A modified project pcb:
the displays have not been loaded
The Atmega 328 is permanently connected
A DIL socket is provided for the Atmega 168.
An additional watch crystal is provided for the Atmega 168
The crystal shares in IO pin with the middle of the 3 user switches.
A track has been cut isolating the switch. (Alternatively the switch could be omitted))
Top USBasp programmer with target device
Bottom left / Top side of PCB111000_1 programmer or project pcb. / DIL socket is used for programmer.
Bottom right / Underside of PCB111000_1 programmer or project PCB showing ATMEGA 328 / No DIL socket (also shows additional crystal)

Note:	USBasp is set to 5V operation, low speed clock. It powers the target device.
CP2102 is a 3V device and is only used to send data from the target device to the PC.

System Soft ware:

Programmer “4_Project_pcb_168_V2.30B”:
Resides on the Atmega 168
Programs the Atmega 328 with the mini-OS and bootloader
Utility to delete the Atmega 168 calibration bytes
Text file containing user prompts required by “4_Project_pcb_168_V2.30B”

Mini-OS/bootloader
Drives the 8 digit 7 segment displays
Programs the Atmega 168 with the user projects
Provides OS services for use by thee user projects

Setting up a new project pcb using the usbasp programmer

The USBasp programmer requires two USB sockets.

Down load the “4_Project_pcb_168_V2.30B” hex file to an Atmega 168.
Assuming a new device it automatically calibrates itself when it first runs
(If it is not new EEPROM locations 0x1FD, E and F should be deleted.)

Solder the device into a Project PCB along with an Atmega 328.
Switch the PCB DPDT slider to the left so that the Atmega 168 runs.
Connect it to a PC running a terminal program
At the “P…….P…….” user prompt press S and download the user prompts to the Atmega168 EEPROM.
When the “P…….P…….” user prompt returns press:
E to program the Atmega 328 EEPROM with a “hello world text file”
P to program the Atmega 328 flash with the mini-OS and bootloader.
The Atmega328 automatically calibrates itself the first time that it runs
Switch the DPDT switch to the right to get the “p/r…..p/r…….” use prompt.
Press “p” to program a user project and “r” to run it.

Setting up a new project pcb using the PCB111000_1 programmer programmer

Program the ATMEGA 328 with the “mini-OS and bootloader” as described above.
Replace the original ATMEGA168 containing the “4_Project_pcb_168_V2.30B” hex file with a new device.
Use the bootloader to put “4_Project_pcb_168_V2.30B” onto the new device.
It will automatically calibrate itself the first time that it runs.
Press “S” at the “P…….P…….” user prompt and download the text file containing the remaining user prompts.

Recalibrating the devices:

Switch the DPDT left and hold SW3 down while powering the pcb. At the “R…….R…….” user prompt press “R” and the Atmega auto cal routine will run.

Load the Atmega168 auto cal or manual cal user projects to recalibrate the Atmega 168.

	Atmega 168		Atmega 328
0x1FF	User value of OSCCAL	0x3FF	User value of OSCCAL
0x1FE	User value of OSCCAL	0x3FE	User value of OSCCAL
0x1FD	Default value of OSCCAL	0x3FD	Default value of OSCCAL
0x1FC	0xFF default / 1: having just programmed a device.	0x3FC	1: Diagnostic mode / else 0
0x1FB	PRN reservation MSB	0x3FB	Display brightness
0x1FA	PRN reservation LSB	0x3FA
0x1F9		0x3F9	1:having just been programmed
0x1F8		0x3F8	PRN reservation LSB
		0x3F6	Alternative if 0x3F8 is broaken

5	Start of text/data space
4	Allocation table for text and data written to the EEPROM using an external programmer. (It starts at address 0x5) / Text saved here y user projects starts at address 0.		Allocation table for text and data written to the EEPROM using an external programmer. (It starts at address 0x5)
3
2
1
0

Path Desktop PC

Path =
C:\WinAVR-20100110\bin;
C:\winAVR-20100110\utils\bin
C:\WINDOWS\system32;
C:\WINDOWS;
C:\WINDOWSSystem32\Wbem;
C:\WINDOWS\System32\WindowsPowerShell\v1.0\;
C:\Program Files\Intel\WiFi\bin\;
C:\Program Files\Common Files\Intel\WirelessCommon\;
C:\Program\Local\Microsoft Files\PuTTy\;
C:WINDOWS\System32\OpenSSH\;
C:\Users\Mark\AppData\Local\Microsoft\WindowsApps;
C:\Users\Mark\AppData|Local\GitHubDesktop\bin;
C:\Users\Mark|AppData\Local\Microsoft\WindowsApps

C:\Program Files (x86)\Atmel\Studio\7.0\toolchain\avr8\avr8-gnu-toolchain\bin\avr-gcc.exe

################################################################################
# Automatically-generated file. Do not edit!
################################################################################

SHELL := cmd.exe
RM := rm -rf

USER_OBJS :=

LIBS :=
PROJ :=

O_SRCS :=
C_SRCS :=
S_SRCS :=
S_UPPER_SRCS :=
OBJ_SRCS :=
ASM_SRCS :=
PREPROCESSING_SRCS :=
OBJS :=
OBJS_AS_ARGS :=
C_DEPS :=
C_DEPS_AS_ARGS :=
EXECUTABLES :=
OUTPUT_FILE_PATH :=
OUTPUT_FILE_PATH_AS_ARGS :=
AVR_APP_PATH :=$$$AVR_APP_PATH$$$
QUOTE := "
ADDITIONAL_DEPENDENCIES:=
OUTPUT_FILE_DEP:=
LIB_DEP:=
LINKER_SCRIPT_DEP:=

# Every subdirectory with source files must be described here
SUBDIRS :=

# Add inputs and outputs from these tool invocations to the build variables
C_SRCS += \
../Proj_2C1.c

PREPROCESSING_SRCS +=

ASM_SRCS +=

OBJS += \
Proj_2C1.o

OBJS_AS_ARGS += \
Proj_2C1.o

C_DEPS += \
Proj_2C1.d

C_DEPS_AS_ARGS += \
Proj_2C1.d

OUTPUT_FILE_PATH +=Proj_2C1_random_LEDs.elf

OUTPUT_FILE_PATH_AS_ARGS +=Proj_2C1_random_LEDs.elf

ADDITIONAL_DEPENDENCIES:=

OUTPUT_FILE_DEP:= ./makedep.mk

LIB_DEP+=

LINKER_SCRIPT_DEP+=

# AVR32/GNU C Compiler
./Proj_2C1.o: .././Proj_2C1.c
@echo Building file: $<
@echo Invoking: AVR/GNU C Compiler : 5.4.0
$(QUOTE)C:\Program Files (x86)\Atmel\Studio\7.0\toolchain\avr8\avr8-gnu-toolchain\bin\avr-gcc.exe$(QUOTE) -x c -funsigned-char -funsigned-bitfields -DDEBUG -I"C:\Program Files (x86)\Atmel\Studio\7.0\Packs\atmel\ATmega_DFP\1.3.300\include" -O1 -ffunction-sections -fdata-sections -fpack-struct -fshort-enums -g2 -Wall -mmcu=atmega168p -B "C:\Program Files (x86)\Atmel\Studio\7.0\Packs\atmel\ATmega_DFP\1.3.300\gcc\dev\atmega168p" -c -std=gnu99 -MD -MP -MF "$(@:%.o=%.d)" -MT"$(@:%.o=%.d)" -MT"$(@:%.o=%.o)" -o "$@" "$<"
@echo Finished building: $<

# AVR32/GNU Preprocessing Assembler

# AVR32/GNU Assembler

ifneq ($(MAKECMDGOALS),clean)
ifneq ($(strip $(C_DEPS)),)
-include $(C_DEPS)
endif
endif

# Add inputs and outputs from these tool invocations to the build variables

# All Target
all: $(OUTPUT_FILE_PATH) $(ADDITIONAL_DEPENDENCIES)

$(OUTPUT_FILE_PATH): $(OBJS) $(USER_OBJS) $(OUTPUT_FILE_DEP) $(LIB_DEP) $(LINKER_SCRIPT_DEP)
@echo Building target: $@
@echo Invoking: AVR/GNU Linker : 5.4.0
$(QUOTE)C:\Program Files (x86)\Atmel\Studio\7.0\toolchain\avr8\avr8-gnu-toolchain\bin\avr-gcc.exe$(QUOTE) -o$(OUTPUT_FILE_PATH_AS_ARGS) $(OBJS_AS_ARGS) $(USER_OBJS) $(LIBS) -Wl,-Map="Proj_2C1_random_LEDs.map" -Wl,--start-group -Wl,-lm -Wl,--end-group -Wl,--gc-sections -mmcu=atmega168p -B "C:\Program Files (x86)\Atmel\Studio\7.0\Packs\atmel\ATmega_DFP\1.3.300\gcc\dev\atmega168p"
@echo Finished building target: $@
"C:\Program Files (x86)\Atmel\Studio\7.0\toolchain\avr8\avr8-gnu-toolchain\bin\avr-objcopy.exe" -O ihex -R .eeprom -R .fuse -R .lock -R .signature -R .user_signatures "Proj_2C1_random_LEDs.elf" "Proj_2C1_random_LEDs.hex"
"C:\Program Files (x86)\Atmel\Studio\7.0\toolchain\avr8\avr8-gnu-toolchain\bin\avr-objcopy.exe" -j .eeprom --set-section-flags=.eeprom=alloc,load --change-section-lma .eeprom=0 --no-change-warnings -O ihex "Proj_2C1_random_LEDs.elf" "Proj_2C1_random_LEDs.eep" || exit 0
"C:\Program Files (x86)\Atmel\Studio\7.0\toolchain\avr8\avr8-gnu-toolchain\bin\avr-objdump.exe" -h -S "Proj_2C1_random_LEDs.elf" > "Proj_2C1_random_LEDs.lss"
"C:\Program Files (x86)\Atmel\Studio\7.0\toolchain\avr8\avr8-gnu-toolchain\bin\avr-objcopy.exe" -O srec -R .eeprom -R .fuse -R .lock -R .signature -R .user_signatures "Proj_2C1_random_LEDs.elf" "Proj_2C1_random_LEDs.srec"
"C:\Program Files (x86)\Atmel\Studio\7.0\toolchain\avr8\avr8-gnu-toolchain\bin\avr-size.exe" "Proj_2C1_random_LEDs.elf"

# Other Targets
clean:
-$(RM) $(OBJS_AS_ARGS) $(EXECUTABLES)
-$(RM) $(C_DEPS_AS_ARGS)
rm -rf "Proj_2C1_random_LEDs.elf" "Proj_2C1_random_LEDs.a" "Proj_2C1_random_LEDs.hex" "Proj_2C1_random_LEDs.lss" "Proj_2C1_random_LEDs.eep" "Proj_2C1_random_LEDs.map" "Proj_2C1_random_LEDs.srec" "Proj_2C1_random_LEDs.usersignatures"

C:\Program Files (x86)\Atmel\Studio\7.0\toolchain\avr8\avr8-gnu-toolchain\bin\avr-gcc.exe