PCB111000_V2 System program tests:

System programs

8_UNO_AVR_Programmer_V3
5_Project_pcb_168_V2.30_Arduino_V2

UNO sketch “8_UNO_AVR_Programmer_V3”
This loads an Atmega 168 with “5_Project_pcb_168_V2.30_Arduino_V2”
The Atmega 168 is then soldered onto PCB 111000_V2 and
is used to program the Atmega 328 with the mini-OS.

UNO programs an ATMEGA168
POR and get user prompt	“s s s s s s s…………….”
Step 1	Press -s- to get
Atmega 168 detected.
Press -p- to program flash, -r- to run target, -d- to clear the target EEPROM or -x- to	escape.
Step 2	Press -p-
Send	5_Project_pcb_168_V2.30_Arduino_V2.ino.eightanaloginputs
Step 3	Follow instructions to Cal device
Get user prompt “P/S P/S P/S………….”
Step 4	press -s- and change BR and send on-chip_strings

Optional steps
At P/S prompt press v to get program name plus version	Project_pcb_168_V2.30_Arduino

Reset UNO to restore user prompt	“s s s s s s s…………….”
Press -s- then -p- then -t- to recalibrate the Atmega 328 and restore user prompt “P/S P/S…...…”

Reset UNO to restore user prompt	“s s s s s s s…………….”
Press -s- then -r- to restore user prompt “P/S P/S P/S………….”

Reset UNO to restore user prompt	“s s s s s s s…………….”
Press -d- to clear “on-chip_strings” and cal bytes from Atmega168 EEPROM

Reprogram the Atmega168 and note that it now requires an initial calibration

Special tests:
Check search for alternative OSCCAL value
Check error print out for error > 3%

Tests
Upload “8_UNO_AVR_Programmer_V3” to a UNO wired to program and calibrate an Atmega 168.

Set BR to 38.4kB.
Get “s s s s s…….” prompt
Press -s-
The UNO responds with:
Atmega 168 detected.
Press -p- to program flash, -r- to run target, -d- to clear the target EEPROM or -x- to escape.
Press -p- and send the “5_Project_pcb_168_V2.30_Arduino_V2” hex file.

If device already calibrated reset the UNO
Press -s- then -r-.
Set 57600 Baud and then press AK
Get “P/S P/S P/S P/S P/S P/S………...” user prompt.
Press -s-
BR 2k4 then AK
Send “on-chip_strings” text file
Chip is now ready to transfer to PCB-111000_V2

Reset UNO and select 38.4kB baud rate.
Press -s- then -d- to clear Atmega 168 eeprom.
Press -s- then -p- and send the “5_Project_pcb_168_V2.30_Arduino_V2” hex file.
Follow instructions to calibrate the Atmega 168.

PCB111000_V2

Setup using the UNO

Upload	“8_UNO_AVR_Programmer_V2” onto a UNO

Use prototype PCB to connect the UNO to an Atmega 168 as follows

Open a terminal program with a baud rate of 38400
Get the following use prompt
“s s s s s s….”
Press ‘s’
The UNO respond with
Atmega 168 detected.
Press -p- to program flash, -e- for EEPROM, -r- to run target or -x- to escape.
Press ‘p’ and send
9C_cal_auto_plus_manual_Arduino_168
Which is found under
Github\UNO_as_an_AVR_programer\9C_cal_auto_plus_manual_Arduino

Press ‘n’ when a text file is requested
Press the UNO reset button Then press ‘s’ followed by ‘t’ to initial calibration using the UNO frequency standard.

After auto cal the following test is printed
Calibrating Atmega 168/P
New OSCCAL value 77
Previous user cal 77
Press 'x' to finish or AOK for manual cal
Press AOK
Select the best User cal value (77 in this case) and enter it.

Reset the UNO	Program the Atmega168 with “Project_pcb_168_V2.30C”
No text file required
Change baud rate to 57600
At prompt “P P P P P………...”
Press ‘s’
Reduce BR to 2.4K and press AK
Send text file “on-chip_strings”
Restore BR

Remove Atmega168 from UNO programming jig and fit to PCB111000
Upload mini_OS
Get p/r prompt
Upload user proj