PCB111000_V2

Setup using the UNO

Upload	“8_UNO_AVR_Programmer_V2” onto a UNO

Use prototype PCB to connect the UNO to an Atmega 168 as follows

Open a terminal program with a baud rate of 38400
Get the following use prompt
“s s s s s s….”
Press ‘s’
The UNO respond with
Atmega 168 detected.
Press -p- to program flash, -e- for EEPROM, -r- to run target or -x- to escape.
Press ‘p’ and send
9C_cal_auto_plus_manual_Arduino_168
Which is found under
Github\UNO_as_an_AVR_programer\9C_cal_auto_plus_manual_Arduino

Press ‘n’ when a text file is requested
Press the UNO reset button Then press ‘s’ followed by ‘t’ to initial calibration using the UNO frequency standard.

After auto cal the following test is printed
Calibrating Atmega 168/P
New OSCCAL value 77
Previous user cal 77
Press 'x' to finish or AOK for manual cal
Press AOK
Select the best User cal value (77 in this case) and enter it.

Reset the UNO	Program the Atmega168 with “Project_pcb_168_V2.30C”
No text file required
Change baud rate to 57600
At prompt “P P P P P………...”
Press ‘s’
Reduce BR to 2.4K and press AK
Send text file “on-chip_strings”
Restore BR

Remove Atmega168 from UNO programming jig and fit to PCB111000
Upload mini_OS
Get p/r prompt
Upload user proj